## Slide 1
Processing of CGGTTS data
Bharath Vattikonda
NPL India
bharath.nplindia@csir.res.in
Secondee at the BIPM
Time Department
Together with the BIPM Time department
July 2025

## Slide 2
BIPM e- Learning Course: https://e-learning.bipm.org/
Filters: Course catalogue -> BIPM -> Time & Frequency
Video tutorial by Dr. Pascale Defraigne, chair of the CCTF WG on GNSS Time Transfer
CCTF Technical Exchange
9th July 2025

## Slide 3
Common Generic GNSS Time Transfer Standard (CGGTTS) data format
(CGGTTS standard)
A standard data format for the GNSS time transfer methods based on pseudorange measurements
The observations recorded are at every 16 minutes interval as per BIPM tracking schedule
Used to perform the Common–View and All-in-View time transfer methods
Time transfer receivers automatically generates the CGGTTS files or else you can use the “r2cggtts’’ ROB software
to convert Rinex data to CGGTTS (available from BIPM ftp with using UTC(k) lab credentials or asking ROB for a copy).
Versions: CGGTTS V1.0 (GPS),
CGGTTS V2.0 (GPS, GLONASS),
CGGTTS V2E (GPS, GLONASS, Galileo, BDS2, QZSS)
Currently one single frequency and one Iono free combination is recognized per GNSS system:
GPS: L1C/A, L1P and L3P Glonass: L1C/A, L1P and L3P
    BDS2 : B1i and L3B Galileo: E1 and L3E QZSS : L1C and L3Q
UTC(k) labs share regularly their CGGTTS files to BIPM for the computation of UTC.
The antenna location should be known better than 3 cm accuracy (through PPP) to match the 0.1 ns numeric precision of
the format
CCTF Technical Exchange
9th July 2025

## Slide 4
Software application: https://cbkt-time.bipm.org/
Source code : https://github.com/TheBIPM/CCTF_CBKT_software
Interactive description of the data format
CCTF Technical Exchange
9th July 2025

## Slide 5
https://cbkt-time.bipm.org/
CCTF Technical Exchange
9th July 2025

## Slide 6
Software application: https://cbkt-time.bipm.org/
Source code : https://github.com/TheBIPM/CCTF_CBKT_software
CCTF Technical Exchange
9th July 2025

## Slide 7
CGGTTS - Analyser:
Demo video : CGGTTS – Analyser: Time & Frequency BIPM CBKT - YouTube
User can upload multiple CGGTTS files and investigate the details of the data
(MJD, REFSYS, frequencies, gaps or jumps in the data )
The interactive plots helps the user for detailed observations
Can perform Common-View and All-in-View time transfer between two receivers' data.
The user has option to perform the CV and AV methods by filtering the data based on
GNSS measurement code (L1P, L1C,L2P etc., )
MJD range
Satellite selection
Outlier selection (as multiples of standard deviation)
Elevation mask (0 to 90 degrees)
The user can download the CSV files of each corresponding plot, for further processing
CCTF Technical Exchange
9th July 2025

## Slide 8
Sum of the weighted REFSYS values of all satellites available, with respect to their elevation angles
All-in-view at each epoch = -
Common – View method
All - in– View method
Weighted Refsys of each receiver
Average of difference between Refsys values at each epoch
Calculations
CCTF Technical Exchange
9th July 2025

## Slide 9
SAT | MJD | STTIME | ELV | REFSYS | FRC
 |  | hhmmss | .1dg | .1ns | 
G10 | 60269 | 140000 | 392 | -94 | L1C
G10 | 60269 | 140000 | 392 | -86 | L1P
G10 | 60269 | 140000 | 392 | 247 | L2C
G10 | 60269 | 140000 | 392 | -69 | L2P
G10 | 60269 | 140000 | 392 | 159 | L5C
G15 | 60269 | 140000 | 351 | -25 | L1C
G15 | 60269 | 140000 | 351 | -8 | L1P
G15 | 60269 | 140000 | 351 | 308 | L2C
G15 | 60269 | 140000 | 351 | -26 | L2P
G18 | 60269 | 140000 | 697 | -17 | L1C
G18 | 60269 | 140000 | 697 | 1 | L1P
G18 | 60269 | 140000 | 697 | 339 | L2C
G18 | 60269 | 140000 | 697 | 4 | L2P
CGGTTS data snippet
Sum of the weighted REFSYS values of all satellites available, with
respect to their elevation angles
Example for calculating: Performance of
Receiver clock - GNSS(time)
= -2.24 ns
At each epoch
CCTF Technical Exchange
9th July 2025

## Slide 10
Example for calculation: Common-view Performance at each epoch
SAT | MJD | STTIME | ELV | REFSYS | FRC
 |  | hhmmss | .1dg | .1ns | 
G10 | 60269 | 1400 | 392 | -94 | L1C
G10 | 60269 | 1400 | 392 | -86 | L1P
G10 | 60269 | 1400 | 392 | 247 | L2C
G10 | 60269 | 1400 | 392 | -69 | L2P
G10 | 60269 | 1400 | 392 | 159 | L5C
G15 | 60269 | 1400 | 351 | -25 | L1C
G15 | 60269 | 1400 | 351 | -8 | L1P
G15 | 60269 | 1400 | 351 | 308 | L2C
G15 | 60269 | 1400 | 351 | -26 | L2P
G18 | 60269 | 1400 | 697 | -17 | L1C
G18 | 60269 | 1400 | 697 | 1 | L1P
G18 | 60269 | 1400 | 697 | 339 | L2C
G18 | 60269 | 1400 | 697 | 4 | L2P
SAT | MJD | STTIME | ELV | REFSYS | FRC
 |  | hhmmss | .1dg | .1ns | 
8 | 60269 | 1400 | 188 | -80 | L1C
32 | 60269 | 1400 | 289 | -63 | L1C
27 | 60269 | 1400 | 595 | -47 | L1C
16 | 60269 | 1400 | 451 | -23 | L1C
23 | 60269 | 1400 | 458 | -70 | L1P
18 | 60269 | 1400 | 267 | -85 | L1P
10 | 60269 | 1400 | 835 | -122 | L1P
26 | 60269 | 1400 | 291 | -40 | L1P
8 | 60269 | 1400 | 188 | -104 | L2P
32 | 60269 | 1400 | 289 | -88 | L2P
27 | 60269 | 1400 | 595 | -68 | L2P
27 | 60269 | 1400 | 595 | -23 | L3P
16 | 60269 | 1400 | 451 | -4 | L3P
GPS Receiver 1 data
(CGGTTS V2E)
GPS Receiver 2 data
(CGGTTS V2)
Common Satellites
Choice of signal Frequency
(L1P)
Refsys values for CV
(units: 0.1 ns)
= 6.1 ns
CCTF Technical Exchange
9th July 2025

## Slide 11
At each epoch
Example for calculating: All-in-view Performance at an epoch
SAT | MJD | STTIME | ELV | REFSYS | FRC
 |  | hhmmss | .1dg | .1ns | 
G10 | 60269 | 1400 | 392 | -94 | L1C
G10 | 60269 | 1400 | 392 | -86 | L1P
G10 | 60269 | 1400 | 392 | 247 | L2C
G10 | 60269 | 1400 | 392 | -69 | L2P
G10 | 60269 | 1400 | 392 | 159 | L5C
G15 | 60269 | 1400 | 351 | -25 | L1C
G15 | 60269 | 1400 | 351 | -8 | L1P
G15 | 60269 | 1400 | 351 | 308 | L2C
G15 | 60269 | 1400 | 351 | -26 | L2P
G18 | 60269 | 1400 | 697 | -17 | L1C
G18 | 60269 | 1400 | 697 | 1 | L1P
G18 | 60269 | 1400 | 697 | 339 | L2C
G18 | 60269 | 1400 | 697 | 4 | L2P
SAT | MJD | STTIME | ELV | REFSYS | FRC
 |  | hhmmss | .1dg | .1ns | 
8 | 60269 | 1400 | 188 | -80 | L1C
32 | 60269 | 1400 | 289 | -63 | L1C
27 | 60269 | 1400 | 595 | -47 | L1C
16 | 60269 | 1400 | 451 | -23 | L1C
23 | 60269 | 1400 | 458 | -70 | L1P
18 | 60269 | 1400 | 267 | -85 | L1P
10 | 60269 | 1400 | 835 | -122 | L1P
26 | 60269 | 1400 | 291 | -40 | L1P
8 | 60269 | 1400 | 188 | -104 | L2P
32 | 60269 | 1400 | 289 | -88 | L2P
27 | 60269 | 1400 | 595 | -68 | L2P
27 | 60269 | 1400 | 595 | -23 | L3P
16 | 60269 | 1400 | 451 | -4 | L3P
GPS Receiver 1 data
(CGGTTS V2E)
GPS Receiver 2 data
(CGGTTS V2)
Choice of signal Frequency
(L1P)
Refsys values for AV
(units: 0.1 ns)
Elevation Angle
(unit 0.1 degrees)
All available Satellites
= -2.24 ns
= -9.43 ns
All-in-view performance = (-2.24) – (-9.43) = 7.19 ns
CCTF Technical Exchange
9th July 2025

## Slide 12
User can upload multiple CGGTTS files and investigate the details of the data
(MJD, Refsys, frequencies, gaps or jumps in the data )
The interactive plots helps the user to select their choice of frequency and
MJD range of the files for detailed observations
To perform the common view and all in view time transfer, two sets of CGGTTS files
need to be uploaded by the user
The user can also select choice of satellites instead of default ALL option, set elevation mask and outlier filter to evaluate the performance of the CV and AV.
The user can also download the CSV files of each corresponding plots
Features
CCTF Technical Exchange
9th July 2025

## Slide 13
CGGTTS – Analyser:
Live Demo
Overview of the Course on e-learning
https://e-learning.bipm.org/
https://cbkt-time.bipm.org/
CCTF Technical Exchange
9th July 2025

## Slide 14
Use case Example: Drift in UTC(k)
Linear drift
Linear drift
CCTF Technical Exchange
9th July 2025

## Slide 15
Use case Example: Jump & Outliers
Jump due to Rx calibration/change in lab setup
Outliers
CCTF Technical Exchange
9th July 2025

## Slide 16
Use case Example: Phase jumps and Gaps
Gaps In data
Phase corrections(steering) applied to UTC(k)
CCTF Technical Exchange
9th July 2025

## Slide 17
Use case Example: Outlier due to one satellite
Sat ID: G25
CCTF Technical Exchange
9th July 2025

## Slide 18
Use case Example: CV with different frequencies
Single frequency (L1P)
Iono free combination (L3P)
CCTF Technical Exchange
9th July 2025

## Slide 19
Use case Example: CV & AV with Same receiver itself (atmospheric effects)
All-in-View [different Frequencies : Iono effect ]
Common –View [different Frequencies : Iono effect]
All-in-View [Same Frequency : Multipath effects]
Common-View [Same Frequency : Multipath effects]
CCTF Technical Exchange
9th July 2025

## Slide 20
Use cases of CGGTTS Analyser and execution steps (1)
Monitor the Performance of the UTC(k)
a. Jump in Time Scale: Jump in weighted Refsys data w.r.t all the constellations at that point of time
b. Jump in the GNSS system: No jump in weighted Refsys data w.r.t other GNSS systems at that point of time
c. Performance of UTC(k) steering : Drift correction in weighted Refsys data w.r.t all GNSS systems
d. Accuracy of UTC(k) w.r.t other UTC(k): Perform CV or AV methods w.r.t another UTC(k) (if you have access to other UTC(k) data}
e. Outliers in the time scale data: Vary the outlier filter, if it exits in all the constellations at same time its an outlier in time scale
Satellite based effect on time link
a. Effect of selected satellites on the time transfer link: Choose required Satellite’s(PRN) and perform AV and CV methods
b. Does one satellite is sufficient for time transfer ? : Select only one satellite and perform the CV and AV method
c. Effect of low altitude satellites on time transfer: Vary the Elevation angle filter and observe the CV and AV links
d. Outliers in a particular satellite data: Vary the outlier limit and select the satellite causing outliers in the link
If you have only one time transfer receiver
a. Atmospheric effects on GNSS signals: Perform CV and AV with different frequencies (Ex: L1C & L2C or L1C & L2P) of same
GNSS system of same receiver of same CGGTTS files
b. Performance of GNSS w.r.t UTC(k): Compare the weighted Refsys data for each GNSS system.
c. Multipath observation: Perform CV and AV with same frequencies (Ex: L1C & L1P)
CCTF Technical Exchange
9th July 2025

## Slide 21
Effect of base line and method of time transfer : {short base line < 60 km, long base line > 1000 km}
Perform CV & AV between short and long base line stations to observe the following
a. Why AV is more suitable for long base lines
b. CV or AV which is more suitable for short base line time transfer
c. Check if Iono-free combination (L3P) is more noisy than single frequency (L1C) CV method in case of short base line
Effect of GNSS frequency on time transfer between two receiver stations:
a. Higher frequency has better performance : Perform CV/AV with L1C (1575.42 MHz) and then with L5C(1176 MHz)
b. Why Ionosphere free combination has better performance than single frequency time transfer : Perform CV/AV with
single frequency (Ex. L1C/L1P/E1/B1i) and then with Iono-free combination (Ex. L3P/L3E/L3Q/L3B) to see the difference
Receiver calibration
a. Offset in AV/CV plots of the receivers connected to common clock indicates the calibration offset between the receivers
Use cases of CGGTTS Analyser and execution steps (1)
CCTF Technical Exchange
9th July 2025

## Slide 22
Thanks for your participation
https://e-learning.bipm.org/
CCTF Technical Exchange
9th July 2025