## Slide 1
Frequency-Comb-Based Time Transfer over Free-Space Links
Laura Sinclair
National Institute of Standards and Technology
Boulder, CO, USA
laura.Sinclair@nist.gov
CCTF Technical Exchange
February 23rd, 2026

## Slide 2: The optical frequency comb
Passively Mode-Locked Laser
Output time of laser pulses and phase relationship between pulses are variable
And set by the dynamics of the laser cavity
In the frequency domain, broad spectral bandwidth
A laser with short pulses with relatively low timing jitter
t

## Slide 3: The optical frequency comb
Fully Self-Referenced Optical Frequency Comb
Stabilize a passively mode-locked laser
Output time of comb pulses and phase relationship between pulses are fixed
And defined by the reference oscillator
.
.
~
Reference Oscillator
Controller
t
Reference Plane
k
k-1
k+1
k+2
k+3
k+4

## Slide 4: The optical frequency comb
Fully Self-Referenced Optical Frequency Comb
Stabilize a passively mode-locked laser
Output time of comb pulses and phase relationship between pulses are fixed
And defined by the reference oscillator
In the frequency domain, a “comb” of optical frequencies
.
~
Reference Oscillator
Controller
t
k
k-1
k+1
k+2
k+3
k+4
f
Frequency Domain
Time Domain
Fourier Transform of many pulses
fn = nfrep+ fceo

## Slide 5: The optical frequency comb
Fully Self-Referenced Optical Frequency Comb
Stabilize a passively mode-locked laser
Output time of comb pulses and phase relationship between pulses are fixed
And defined by the reference oscillator
In the frequency domain, a “comb” of optical frequencies
An ultra-precise fixed ruler for time and frequency
~
Reference Oscillator
Controller
t
k
k-1
k+1
k+2
k+3
k+4
f
Frequency Domain
Time Domain
Fourier Transform of many pulses
Broadband, narrow linewidth, few-fs timing jitter
Nobel Prize 2005
T. Hänsch
J. Hall

## Slide 6: Frequency Combs Make Timing Comparisons at 18-Digits Possible
Clock or reference oscillator
Comb with pulse output
Site A
Timing Comparison
Clock or reference oscillator
Comb with pulse output
Site B
Optical Reference Oscillator
Define a local timescale with sub-femtosecond precision
Generate a frequency reference with sub 10-18 precision
Sets pulse spacing
~5ns
Controller:
Count pulses
Ticks of local timescale defined by pulses crossing this reference plane
“Dual-comb” measurements:
Attosecond-level precision on pulse arrival timing

## Slide 7: Free-space Time Transfer Challenges
Clock or reference oscillator
Comb with pulse output
Timing Comparison
Site A
Clock or reference oscillator
Comb with pulse output
Site B
Free-space channel challenges
Optical Reference Oscillator

## Slide 8: Free-space Time Transfer Challenges
Clock or reference oscillator
Comb with pulse output
Timing Comparison
Site A
Clock or reference oscillator
Comb with pulse output
Site B
Free-space channel challenges
Intensity fluctuations (scintillation)- orders of magnitude variations in received power
Optical Reference Oscillator

## Slide 9: Free-space Time Transfer Challenges
Clock or reference oscillator
Comb with pulse output
Timing Comparison
Site A
Clock or reference oscillator
Comb with pulse output
Site B
Free-space channel challenges
Intensity fluctuations (scintillation)- orders of magnitude variations in received power
2. Time-of-flight fluctuations- picosecond level fluctuations in pulse arrival time
Optical Reference Oscillator

## Slide 10: Free-space Time Transfer Challenges
Clock or reference oscillator
Comb with pulse output
Timing Comparison
Site A
Clock or reference oscillator
Comb with pulse output
Site B
Free-space channel challenges
Intensity fluctuations (scintillation)- orders of magnitude variations in received power
2. Time-of-flight fluctuations- picosecond level fluctuations in pulse arrival time
Optical Reference Oscillator
Solved by: operation at the quantum-limit, long integration time and ns-scale ambiguity range
Solved by: two-way operation

## Slide 11: Expanding the Toolbox to Handle Long Distances: The Time Programmable Frequency Comb
~
Reference Oscillator
Controller
Digital Timing Commands
The Time Programmable Frequency Comb
Combine a self-referenced comb with modern digital control
Output time of comb pulses and phase relationship between pulses can be adjusted to an arbitrary user-defined value with attosecond-level accuracy
Values are still defined by the reference oscillator
A numerically controlled optical oscillator
E.D Caldwell, L.C. Sinclair, N.R. Newbury and J.-D. Deschenes, “The time-programmable frequency comb and its use in quantum-limited ranging”, Nature 610 667-673 (2022)

## Slide 12: Time Programmable Comb -> Tracking Comb A quantum limited timer
+Δt
Tracking Comb (local oscillator)
Signal Comb
(Remote site)
Controls: Move +Δt
Measure
Heterodyne Voltage
Caldwell, E. D., Sinclair, L. C., Newbury, N. R. & Deschenes, J.-D. The time-programmable frequency comb and its use in quantum-limited ranging. Nature 610, 667–673 (2022).
Timing Comparison
Tracking Local Oscillator (LO) Comb
Time Offset of signal pulse
Incoming signal pulses (remote)
Feedback

## Slide 13: Time Programmable Comb -> Tracking Comb A quantum limited timer
TPFC
LPF
Digital PLL
Quantum
limited
timer
clock
ref.
0.000 000 623 ns
Measurement time: 38 μseconds
time offset
clock optical reference
incoming pulse train
(<< 1 photon per pulse)
unbalanced MZI + balanced heterodyne detection (BPD)
26 kHz

## Slide 14: Two-way optical time transfer: Precise detection plus removal of propagation noise
Clock or reference oscillator
Optical Reference Oscillator
Two-way combination cancels common time-of-flight noise and has attosecond precision from time programmable comb measurement:
Comb with pulse output
Site A
Clock or reference oscillator
Comb with pulse output
Site B
Free-space channel
Single-mode reciprocal link
tB→A=Tflight - Dtclock
tA→B=Tflight + Dtclock
Optical Timing Comparison
Optical Timing Comparison

## Slide 15: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air
Octosig
Folded link geometry
Truth by direct “shorted” comparison at Mauna Loa Observatory
Link loss ~90 dB!
E. D. Caldwell et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)
Site support: University of Hawaii and NOAA

## Slide 16: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air
Octosig
Folded link geometry
Truth by direct “shorted” comparison at Mauna Loa Observatory
Link loss ~90 dB!
E. D. Caldwell et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)
Site support: University of Hawaii and NOAA

## Slide 17: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air – Some Numbers
Clock or reference oscillator
Optical Reference
Comb with pulse output
Tracking Comb Detection
Site A
Clock or reference oscillator
Comb with pulse output
Site B
Free-space channel
Tracking Comb Detection
Single-mode reciprocal link
tB→A=Tflight - Dtclock
tA→B=Tflight + Dtclock
feedback
E. D. Caldwell et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)
195 THz
Free-running
Cavity-stabilized laser
200 MHz
Repetition rate
200 MHz
Repetition rate
195 THz
Free-running
Cavity-stabilized laser
4 mW
Centered at 1560 nm
4 mW
Centered at 1560 nm

## Slide 18: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air
fiber shorted
Caldwell, E. D. et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)

## Slide 19: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air
fiber shorted
2 km
Quantum limit
(2km power)
Caldwell, E. D. et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)

## Slide 20: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air
Sub-femtosecond synchronization
Shot-noise limited SNR
  270 fW threshold (~1/100 photons per pulse)
4 mW launch
Caldwell, E. D. et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)
1 second average
10 second average

## Slide 21: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air
2 km
300 km, 4 mW launch
fiber shorted
Quantum limit
(2km power)
Caldwell, E. D. et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)

## Slide 22: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air
Sub-femtosecond synchronization
Shot-noise limited SNR
  270 fW threshold (~1/100 photons per pulse)
4 mW launch
Caldwell, E. D. et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)
40 uW launch
1 second average
10 second average
1 second average
10 second average

## Slide 23: Evaluation of Tracking Comb-based Time Transfer: Fractional Frequency Instability- 2km to 300 km
2 km
300 km, 4 mW launch
300 km, 40 μW launch
fiber shorted
Quantum limit
(2km power)
Caldwell, E. D. et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)

## Slide 24: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air
300 km, 4 mW launch
300 km, 40 μW launch
Quantum limit
(rec. power from 4 mW launch)
Quantum limit
(rec. power from 40 μW launch)
While the full synchronized signal is not quantum limited, the acquisition and measurement system still is
Synchronization is limited by extra turbulence noise
Caldwell, E. D. et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)

## Slide 25: Optical Time Transfer at the Quantum Limit Over 300 km of Turbulent Air
fiber shorted
2 km
300 km, 4 mW launch
300 km, 40 μW launch
State-of-the-art transportable clocks [1]
State-of-the-art laboratory clocks [2]
[1] Takamoto, M. et al. Test of general relativity by a pair of transportable optical lattice clocks. Nature Photonics 1–5 (2020).
[2] Boulder Atomic Clock Optical Network (BACON) Collaboration et al. Frequency ratio measurements at 18-digit accuracy using an optical clock network. Nature 591, 564–569 (2021).
E. D. et al. Quantum-limited optical time transfer for future geosynchronous links. Nature 618, 721–726 (2023)
Quantum limit
(2km power)

## Slide 26: Looking to the Future
  Longer spans using ground-to-satellite links, good-enough oscillators on-board satellites and state-of-the-art ground clocks
  Modeling suggests existing tracking comb optical time transfer with minimal modifications would work (E.D. Caldwell et al, APL Photonics, 9, 016112 (2024)
  Re-envisioning tracking comb optical time transfer to support the Doppler shifts and slew rates of ground-to-satellite links (collaboration with University of Western Australia)
  Terrestrial networks using the exquisite precision of atomic optical clocks
    Peaks to Plains Relativistic Redshift (R2P2) Collaboration -- a comparison of Yb lattice clocks separated by 2700 m of elevation (successful hardware shakedown summer 2025)

## Slide 27: Thanks for listening. Questions?
Upcoming talks:
  EFTF: Emily Caldwell and Shawn McSorely (University of Western Australia)
  IFCS: Fabrizio Giorgetta and myself
Recent Review Paper:
E.D. Caldwell, T. M. Triano, L.C. Sinclair, “High-precision optical time and frequency transfer”, Advances in Optics and Photonics, 17, 375-440 (2025)
Funding support over the years from:
Site specific support from:
NTIA, NOAA, and the University of Hawaii
QSEC-TAQS
Current Optical Time Transfer Project
NIST
Emily Caldwell, Ian Coddington,
Christopher Dennis, Fabrizio Giorgetta, Laura Sinclair,
William Swann, and Theodora Triano
OctoSig Consulting/Waxwing Instruments
Hugo Bergeron, Jean-Daniel Deschenes
Past OTT Project Members
Esther Baumann, Hugo Bergeron, Martha Bodine,
Mick Cermak, Allie Christensen, Jennifer Ellis,
Christopher Flood (CU Aerospace), Isaac Khader,
Paritosh Manurkar, Nathan Newbury,
Sarah Stevenson, Benjamin Stuhl (Space Dynamics Laboratory), and Saad Syed
27