## Slide 1
Research on Quantum Metrology
at KRISS
2017. 10. 19 BIPM
Jinhee Kim
Quantum Metrology Institute Director

## Slide 2
Quantum (Phase) Coherence
Quantized Particle
Quantum Metrology?
Josephson Voltage Standards (JVS)
Quantum Hall Resistance Standards (QHR)
Superconducting Quantum Interferometer (SQUID)
Qubit, BEC, …
Single Electron Transistor (SET)
Single Photon Source/Counter
Single Phonon, Single Molecule, …
Quantized Energy Level
Atomic Clock

## Slide 3
SET & Quantum Metrology Triangle (QMT)
U / G∙I∙R = 1 + dQMT
f
U
I
JVS
Graphene
QHR-array
SET-quantum current sources
in parallel
I = Nef
(N is # of SET)
U = f/KJ
CCC
G
R
R = MRK
(M is # of QHR)
Josephson
effect
SET effect
Quantum Hall effect
Check the consistency of QMT with 10-8 uncertainty
GaAs/AlGaAs 2DEG
DVexit

## Slide 4
Quantum Candela – Optics Base
Single Photon Source based on Silicon Vacancy in Nano-Diamond
Single Photon Detectors based on detection Efficiency Measurement

## Slide 5
Quantum Candela – Device Base
MIQC (Monolithic Integrated Quantum Circuits)
single-photon source
single-photon detector
single-photon processor

## Slide 6
Optical Lattice Clock
The most stable frequency reference
Ytterbium atoms trapped in optical lattice
Ultra stable oscillator
1 Hz linewidth laser
Optical to RF converter
Optical frequency comb
171Yb Optical lattice clock toward 10-18 uncertainty
Yb-KRISS systematic uncertainty
2017
2020
Ref. CRP16-506(2015)
Yb KRISS
Sr NICT
Satellite clock comparison
fYb/fSr by TWCP (KRISS-NICT)= 1.207 507 039 343 337 86(70)

## Slide 7
Nano Mechanical Oscillator
Single phonon measurement and control
single-phonon resonator
(nanomechanical oscillator near ground state)
microwave photons
(phonon measurement & control)
superconducting circuit
(photon-phonon coupling)

## Slide 8
Our Strategy
Restructuring our Organization (4 Div. → 3 Div. + 2 Inst.)
Project-Based Research Organization: Institute of Quantum Metrology (IQT)
Some researchers have positions both in IQT and Div. of Physical Metrology.
Strengthening our Quantum Device Activities (long-term plan)
Josephson, Quantum Hall, SET, Nano Mechanical Oscillator,
Single Photon Source/Detector, Chip-Scale Atomic Clock, …
Networking
International & Domestic

## Slide 9
Thank You